## Slide 1
CAGAYAN STATE UNIVERSITY · CARIG CAMPUS
Development of a Localized Real-Time Frequency
Monitoring System for Structural Health Monitoring
Using MEMS IMUs and ESP32
PROPOSAL DEFENSE
Jan Clyde Talosig
Bachelor of Science in Electronics Engineering · August 2026

## Slide 2
OVERVIEW
What We'll Cover
1
Introduction
Background
Problem & Objectives
Framework
Scope & Significance
2
Related Literature
Key Findings
Synthesis
3
Methodology
System Design
Data Collection
Data Analysis
Presentation Overview
Proposal Defense — BSECE 2026

## Slide 3
CHAPTER I
Background of the Study
1
Bridges Under Strain
Philippine bridges absorb constant stress from traffic, typhoons, flooding, and earthquakes — day after day.
2
Damage Hides Until It's Late
Cracks and fatigue often aren't visible on inspection, but they do shift how a structure vibrates.
3
Existing Tools Are Costly
Imported monitoring systems and accelerometers remain out of budget for most local government units.
4
A Low-Cost Local Alternative
This study builds an ESP32 + MEMS IMU device that tracks frequency shifts in real time, at a fraction of the cost.
Background of the Study
Proposal Defense — BSECE 2026

## Slide 4
CHAPTER I
Background — Why Buntun Bridge
This study will be tested on Buntun Bridge, Tuguegarao City — the 2nd longest river bridge in the Philippines next to the new Camalaniugan Bridge, and a structure with a documented, ongoing deterioration concern.
56+ yrs
In service since 1969 — steel truss, 1,369 m span
₱101.3M
Spent on DPWH retrofit & strengthening in 2023
15-ton
Vehicle limit imposed in March 2025 over new deterioration
Despite the 2023 retrofit, DPWH engineers reported fresh cracks and holes in the deck in 2025 — showing that periodic inspection alone isn't catching deterioration early enough. That is precisely the gap this study's real-time monitoring approach is meant to close.
Source: DPWH Region II; Philippine Information Agency; GMA Regional TV (2023–2025)
Background — Local Context
Proposal Defense — BSECE 2026

## Slide 5
CHAPTER I
Problem Statement & Objectives
RESEARCH QUESTION
STUDY OBJECTIVE
1
1
How can vibration data be captured and processed in real time?
Develop a real-time system to acquire and process bridge vibration data.
2
2
How reliably can the system extract the bridge's resonant frequency from that data?
Extract and track resonant frequency using signal processing methods.
3
3
How can results be shown to users in a clear, real-time way?
Develop a live web-based dashboard for monitoring and visualization.
Problem Statement & Objectives
Proposal Defense — BSECE 2026

## Slide 6
CHAPTER I
Conceptual Framework
INPUT
Bridge structural vibrations
Dynamic loads (traffic, wind)
Triaxial acceleration (X, Y, Z)
Raw signals from MPU-6050
Ambient excitation forces
➜
PROCESS
Sensor calibration & offset correction
Moving Average Filter (noise cleanup)
Hamming windowing
FFT computation
Peak frequency detection
RMS vibration energy calculation
➜
OUTPUT
Dominant resonance frequency (Hz)
RMS vibration intensity
Normalized vibration index
OK / WARN / CRIT alerts
Web dashboard visualization
CSV data log
Conceptual Framework
Proposal Defense — BSECE 2026

## Slide 7
CHAPTER I
Scope & Significance
SCOPE OF THE STUDY
Field testing planned on Buntun Bridge, Tuguegarao
Focused on real-time frequency monitoring only
Sensors mounted non-invasively — no structural alteration
Site access & schedule subject to DPWH/LGU coordination
Not a full bridge diagnosis or repair tool
WHY IT MATTERS
Directly applicable to a bridge already flagged for deterioration
A low-cost alternative to expensive imported systems
Gives engineers an early-warning tool between inspections
Built entirely with accessible, local components
Scope & Significance
Proposal Defense — BSECE 2026

## Slide 8
CHAPTER II
Related Literature — Claims & Evidence
CLAIM
SUPPORTING EVIDENCE
Vibration monitoring detects structural damage early
Accelerometer-based systems successfully detected cracks in bridge structures (Sales et al., 2022)
Frequency shifts are a valid indicator of damage
Changes in natural frequency are an established indicator of deterioration (Zhang & Li, 2023; Salawu, 1997)
Low-cost SHM hardware can still perform reliably
Budget SHM systems proven feasible for real infrastructure use (Komarizadehasl et al., 2022)
ESP32 + MEMS sensors suit continuous field use
ESP32 handles real-time sensing reliably (El-Khozondar et al., 2024); MEMS sensors are accurate & low-power (Patel & Singh, 2025)
FFT is an accepted method for frequency extraction
FFT-based frequency analysis is a long-established SHM technique (Doebling, Farrar & Prime, 1998)
Related Literature — Claims & Evidence
Proposal Defense — BSECE 2026

## Slide 9
CHAPTER II
Synthesis
THE GAP
The technology to build affordable SHM systems clearly exists — but very few local, low-cost, real-time solutions have actually been built and tested for Philippine bridges.
THIS STUDY'S FIT
This study brings together three proven, individually well-supported pieces — MEMS sensors, ESP32 processing, and FFT-based frequency analysis — into one complete, low-cost, real-time monitoring device built for local conditions.
Synthesis
Proposal Defense — BSECE 2026

## Slide 10
CHAPTER III
System Architecture & Design
1
Sensors
3 IMU sensors mounted on the test structure
➜
2
Processing Unit
Microcontroller filters signal & extracts frequency
➜
3
Dashboard
Results shown live on a web-based display
Built on an ESP32-S3 microcontroller and MPU-6050 motion sensors — all off-the-shelf, low-cost parts.
System Architecture & Design
Proposal Defense — BSECE 2026

## Slide 11
CHAPTER III
Data Collection & Analysis
1
Data Collection
Sensors mounted on the test structure
Vibration readings taken across repeated sessions
Data logged automatically for later review
2
Data Analysis
Frequency extracted from each session's readings
Results compared across sessions for consistency
Focus is on repeatable, trustworthy results — not lab-grade precision
Data Collection & Analysis
Proposal Defense — BSECE 2026

## Slide 12
Thank You
Questions & Discussion
Jan Clyde Talosig
Cagayan State University – Carig Campus · College of Engineering and Architecture