## Slide 1
61,892
Total Data Records Logged
100%
Transmission Success Rate
5.57–5.94
Hz — Structural Resonance (All-Axis)
CAGAYAN STATE UNIVERSITY · CARIG CAMPUS
COLLEGE OF ENGINEERING AND ARCHITECTURE
DEVELOPMENT OF A LOCALIZED
REAL-TIME FREQUENCY MONITORING
SYSTEM FOR STRUCTURAL HEALTH
MONITORING USING MEMS IMUs AND ESP32
A Cost-Effective, Embedded IoT Approach to Bridge Vibration Analysis
Bachelor of Science in Electronics Engineering · April 2026
Researchers:
Jan Clyde Talosig
Shamel Alliyah Senosn
Ayessa Marie Ramos
Gemini Almoite
Cagayan State University – Carig Campus · Tuguegarao City, Cagayan
Date of Submission: April 2026

## Slide 2
PRESENTATION OVERVIEW
Localized Real-Time Frequency Monitoring System for Structural Health Monitoring
CH. I
Introduction
› Background of the Study
› Conceptual Framework (IPO)
› Problem Statements & Objectives
› Scope and Delimitations
› Significance of the Study
CH. II
Review of Literature
› Structural Health Monitoring
› MEMS Sensors & ESP32
› FFT & Signal Processing
› IoT-Based SHM Systems
› Synthesis of Literature
CH. III
Methodology
› Research Design
› Hardware & Software Components
› Detection Algorithm
› Emergency Alert Pipeline
› Validation Protocols
CH. IV
Results & Conclusions
› IMU Performance Results
› Frequency Extraction Data
› System Functionality
› Overall Effectiveness
› Conclusions & Recommendations
Frequency Monitoring SHM System | Cagayan State University – Carig Campus | BSECE 2026

## Slide 3
CHAPTER I — INTRODUCTION
Background of the Study
Bridges are critical infrastructure in the Philippines — highly exposed to earthquakes, typhoons, flooding, and soil erosion. Structural deterioration must be detected early to prevent catastrophic failure.
Frequency-based Structural Health Monitoring (SHM) is a reliable method for detecting structural changes. Natural and resonant frequencies shift measurably when damage such as cracks, corrosion, or joint degradation occurs.
Existing SHM systems in the Philippines rely on costly imported technologies, limiting deployment to large-scale projects. Many bridges depend on periodic visual inspections that miss early-stage deterioration.
This study develops a localized, real-time frequency monitoring system using MEMS IMU sensors and an ESP32-S3 — cost-efficient, portable, and designed for Philippine bridge conditions.
₱ LOW
Cost vs. Imported SHM Systems
3-Axis
MPU-6050 Vibration Sensing Per Node
167 Hz
Sampling Rate (Nyquist: 83.5 Hz)
1024-pt
FFT Window with Hamming Windowing
Frequency Monitoring SHM System | Cagayan State University – Carig Campus | BSECE 2026

## Slide 4
CHAPTER I — INTRODUCTION
Problem Statements & Objectives
RESEARCH QUESTIONS
STUDY OBJECTIVES
Q1
What device can be developed for monitoring the structural health of a bridge through vibration analysis?
Q2
How can resonance frequency be extracted from bridge vibration signals despite the presence of noise and unwanted frequency components?
Q3
How can the developed device provide real-time monitoring and visualization of structural vibration behavior?
Q4
How effective is the developed device in detecting and representing vibration characteristics that may indicate possible structural anomalies?
1
Develop a real-time frequency monitoring system using MEMS-based IMU sensors and ESP32-S3 microcontroller.
2
Acquire vibration signals and extract natural and resonant frequencies using FFT-based signal processing techniques.
3
Design and implement a real-time visualization interface for monitoring frequency behavior via a web-based dashboard.
4
Evaluate system performance in detecting frequency variations that may indicate structural anomalies in bridge structures.
Frequency Monitoring SHM System | Cagayan State University – Carig Campus | BSECE 2026

## Slide 5
CHAPTER I — INTRODUCTION
Conceptual Framework — IPO Model
INPUT
› Bridge Structural Vibrations
› Dynamic Loads (Traffic, Wind, Environmental)
› Triaxial Acceleration Data (X, Y, Z)
› Raw IMU Signals from MPU-6050 Sensors
› Ambient Excitation Forces
→
PROCESS
› IMU Calibration & Offset Correction
› Moving Average Filter (MAF) Pre-Processing
› Hamming Windowing Function
› 1024-Point FFT Computation
› Peak Frequency Detection
› RMS Vibration Energy Calculation
→
OUTPUT
› Dominant Resonance Frequency (Hz)
› RMS Vibration Intensity
› Normalized Vibration Index
› CRIT / WARN / OK State Alerts
› Web Dashboard Visualization
› CSV Data Log (LittleFS)
Frequency Monitoring SHM System | Cagayan State University – Carig Campus | BSECE 2026

## Slide 6
CHAPTER I — INTRODUCTION
Scope and Delimitations
01
System Coverage & Environment
› Focuses on frequency-based SHM — vibration signal acquisition, FFT processing, and frequency extraction
› Hardware: ESP32-S3 microcontroller + 3x MPU-6050 IMU sensors on a custom PCB
› Testing performed in a laboratory-controlled environment at CSU–Carig Campus (AY 2024–2025)
› System limited to small-scale structural test bed — not deployed on an actual full-scale bridge
02
Technical Constraints
› Hardware constraints include processing speed, memory capacity, and MPU-6050 sensor resolution
› Sampling rate: 167 Hz — Nyquist limit of 83.5 Hz; suitable for 2–80 Hz bridge vibration modes
› Environmental factors (temperature, humidity, EMI) not fully incorporated into the analysis
› System outputs frequency data but does not perform structural diagnosis or predict failure
03
Exclusions
› Structural load analysis, predictive modeling, and repair recommendations are excluded
› No full-scale field deployment; validation confined to controlled prototype testing
› Multi-bridge or multi-node IoT network deployment is outside the current scope
› Expert evaluation limited to system functionality testing — no formal jury survey conducted
Frequency Monitoring SHM System | Cagayan State University – Carig Campus | BSECE 2026

## Slide 7
CHAPTER I — INTRODUCTION
Significance of the Study
01
Core Innovation & Technical Contribution
This study develops a cost-effective, localized SHM system using accessible MEMS technology and the ESP32-S3 platform — providing a practical alternative to expensive imported solutions. The integration of 1024-point Hamming-windowed FFT, FreeRTOS dual-core scheduling, and real-time web visualization demonstrates a full-stack embedded IoT approach to bridge monitoring.
› Enables early detection of structural anomalies through continuous resonance frequency tracking
› Contributes to academic literature on embedded SHM systems for resource-limited environments
› Promotes technological independence using locally accessible, off-the-shelf components
02
Key Beneficiaries & Applications
The system benefits multiple stakeholders across engineering, government, and research sectors by offering real-time, data-driven infrastructure monitoring at low deployment cost.
› Engineers & Inspectors: Supplementary continuous monitoring tool enabling early anomaly identification
› Government Agencies: Supports data-driven decisions for bridge maintenance, safety planning
› Academic Community: Reference framework for future IoT-based and embedded SHM research
› Local Communities: Improved bridge safety monitoring in resource-constrained Philippine settings
Frequency Monitoring SHM System | Cagayan State University – Carig Campus | BSECE 2026

## Slide 8
CHAPTER III — METHODOLOGY
System Architecture & Research Design
RESEARCH DESIGN
· Developmental-Evaluative Research Design
· Phase 1: System Design → Phase 2: Firmware Dev → Phase 3: Data Collection → Phase 4: Evaluation
· Study Area: Laboratory environment, CSU–Carig Campus, Tuguegarao City, Cagayan
· FreeRTOS dual-core scheduling: Core 0 (acquisition) / Core 1 (FFT + web server)
HARDWARE COMPONENTS
ESP32-S3
Dual-core MCU; FFT, FreeRTOS, WebServer
MPU-6050 ×3
6-axis MEMS IMU; triaxial acceleration (I²C)
Custom PCB
Power regulation, sensor headers, communication
LittleFS Flash
Onboard CSV data logging (time-domain + FFT)
Wi-Fi (STA/AP)
20 Hz polling endpoint (/data) for dashboard
SOFTWARE STACK
Arduino IDE / PlatformIO
Firmware development environment
FreeRTOS
Real-time dual-core task scheduling
arduinoFFT Library
1024-point FFT with Hamming windowing
WebServer (ESP32)
Synchronous HTTP server for dashboard delivery
Three.js (WebGL)
3D fabric-ripple bridge heatmap (96×96 mesh)
LittleFS
Onboard flash filesystem for CSV logging
Frequency Monitoring SHM System | Cagayan State University – Carig Campus | BSECE 2026

## Slide 9
CHAPTER III — METHODOLOGY
Detection Algorithm — FFT Signal Processing
PRIMARY
STAGE 1: DATA ACQUISITION
Sampling Rate: 167 Hz
I²C Bus (ADO pin multiplexing)
3x MPU-6050 polled sequentially
Core 0 — deterministic timing
→
STAGE 2: PRE-PROCESSING
Moving Average Filter (MAF)
Hamming Window Function
Offset calibration applied
Noise floor suppression
→
STAGE 3: FFT COMPUTATION
1024-point FFT (arduinoFFT)
Frequency resolution: 0.163 Hz
Peak bin detection algorithm
Dominant frequency extracted
SECONDARY A
TRIGGER: RMS Threshold Detection
RMS acceleration computed per axis. Thresholds define OK / WARN / CRIT states. CRIT alert fires when RMS exceeds critical level. No false alerts observed during idle periods.
SECONDARY B
TRIGGER: Cross-Axis Coupling Response
Multi-directional energy propagation detected across axes during single-axis excitation. Y-axis peak (1.6265g) exceeded X-axis during X-excitation. Confirms realistic structural coupling behavior.
Frequency Monitoring SHM System | Cagayan State University – Carig Campus | BSECE 2026

## Slide 10
CHAPTER III — METHODOLOGY
Data Acquisition & Monitoring Pipeline
1
📌
Sensor Placement
Three MPU-6050 IMUs mounted on structurally significant points using rigid fasteners to minimize mounting-induced noise.
→
2
⚡
System Init
ESP32-S3 initializes I²C bus, calibrates each IMU at rest, computes offsets, and establishes the WebServer endpoint.
→
3
🌊
Ambient Vibration
Data collected under ambient excitation (OMA method) using natural traffic, wind, and environmental forces — no artificial input.
→
4
🔬
Signal Processing
MAF pre-conditioning → Hamming windowing → 1024-point FFT → Peak bin detection. Core 1 handles all DSP tasks deterministically.
→
5
📡
Visualization
Web dashboard polled at 20 Hz via /data endpoint. 3D fabric-ripple simulation with CRIT/WARN/OK color-coded state indicators.
✓ 100% Transmission Success Rate across all test sessions
✓ Zero data loss or packet drops observed during any session
✓ FreeRTOS dual-core scheduling ensures deterministic acquisition and processing
✓ Dual-stage smoothing (LPF + LERP) eliminates visual jitter on dashboard
✓ Self-hosted dashboard — no external server infrastructure required
Frequency Monitoring SHM System | Cagayan State University – Carig Campus | BSECE 2026

## Slide 11
CHAPTER III — METHODOLOGY
Validation Protocols & Reliability Testing
01
Repeatability Testing
The system was subjected to repeated measurement sessions under similar ambient conditions to assess extraction consistency.
▸ Standard deviation of peak frequency values computed across sessions to quantify repeatability
▸ Y-Axis session achieved median 5.93 Hz vs. mean 5.98 Hz — difference of only 0.05 Hz
▸ Demonstrates algorithmic stability under sustained, single-axis excitation
02
Sensor Calibration Verification
Each MPU-6050 was calibrated prior to deployment with static baseline readings and computed offsets.
▸ Post-calibration residual noise floors verified within manufacturer-specified range
▸ Hamming window effectiveness verified by comparing raw vs. windowed FFT outputs
▸ Spectral leakage reduced significantly confirming filter adequacy for frequency isolation
03
Cross-Sensor Consistency
Frequency outputs from all three sensor nodes were compared to identify consistent modal peaks vs. localized noise.
▸ X, Y, Z axes in All-Axis session converged at 5.57, 5.94, 5.94 Hz — strong modal agreement
▸ Consistent cross-axis resonance detection distinguishes structural modes from artifacts
▸ Single-axis sessions confirmed ~100% frequency extraction success rate during excitation
Frequency Monitoring SHM System | Cagayan State University – Carig Campus | BSECE 2026

## Slide 12
CHAPTER IV — RESULTS & DISCUSSION
Results: IMU Performance & Data Transmission
Test Session | Axis | Total Records | Active (RMS>0) | Peak RMS (g) | CRIT Events
All-Axis | X | 5,347 | 2,157 (40.3%) | 1.0566 | 653
All-Axis | Y | 5,347 | 751 (14.0%) | 0.9870 | 569
All-Axis | Z | 5,345 | 793 (14.8%) | 1.1485 | 581
X-Axis Excitation | X | 4,661 | 120 (2.6%) | 0.8514 | 6
X-Axis Excitation | Y (coupled) | 4,661 | 370 (7.9%) | 1.6265 | 628
Y-Axis Excitation | Y | 5,335 | 2,577 (48.3%) | 1.0167 | 2,514
Z-Axis Excitation | Z | 5,289 | 448 (8.5%) | 0.6868 | 17
61,892
Total Records Logged Across All Sessions
100%
Transmission Success (Zero Data Loss)
~20 Hz
Frontend Polling Rate (50ms Update Cycle)
4 Sessions
All Test Sessions Completed Without Failure
Frequency Monitoring SHM System | Cagayan State University – Carig Campus | BSECE 2026

## Slide 13
CHAPTER IV — RESULTS & DISCUSSION
Results: Resonance Frequency Extraction
Test Session | Axis | Non-Zero Windows | Median Freq (Hz) | Mean Freq (Hz) | Dominant Range | Extraction Rate
All-Axis | X | 1,605 | 5.57 | 7.67 | 5–8 Hz | 74.4%
All-Axis | Y | 562 | 5.94 | 6.24 | 5–7 Hz | 74.8%
All-Axis | Z | 581 | 5.94 | 6.65 | 5–7 Hz | 73.3%
X-Axis Excitation | X | ~120 | 3.06 | 14.87 | 3–7 Hz | ~100%
X-Axis Excit. | Y (coupled) | ~370 | 3.75 | 5.40 | 3–6 Hz | ~100%
Y-Axis Excitation | Y | 2,577 | 5.93 | 5.98 | 5–7 Hz | 100%
Z-Axis Excitation | Z | ~448 | 4.38 | 5.49 | 4–6 Hz | ~100%
5.57–5.94
Hz Median Resonance (All-Axis Session)
5.93 Hz
Y-Axis Session Median (0.05 Hz Spread)
2–10 Hz
Bridge Mode Range — System Values Confirmed
~100%
Extraction Rate Under Active Excitation
Frequency Monitoring SHM System | Cagayan State University – Carig Campus | BSECE 2026

## Slide 14
CHAPTER IV — RESULTS & DISCUSSION
Results: System Functionality & Web Interface
Test Session | Total Records | Successful Transmissions | Data Loss Events | Success Rate
All-Axis | 16,039 | 16,039 | 0 | ✓ 100%
X-Axis Excitation | 13,982 | 13,982 | 0 | ✓ 100%
Y-Axis Excitation | 16,004 | 16,004 | 0 | ✓ 100%
Z-Axis Excitation | 15,867 | 15,867 | 0 | ✓ 100%
TOTAL | 61,892 | 61,892 | 0 | 100%
Chart: CRIT Events per Session
| All-Axis X | All-Axis Y | All-Axis Z | Y-Axis Session
CRIT Events | 653 | 569 | 581 | 2514
✓ End-to-End Confirmation: All 4 test sessions completed with ZERO data loss, ZERO false alerts during idle periods, and continuous 20 Hz dashboard responsiveness throughout.
97.6%
CRIT Alert Rate — Y-Axis Max Excitation Session
50 ms
Dashboard Update Interval at 20 Hz Polling
0
Data Loss Events Across All 61,892 Transmissions
Frequency Monitoring SHM System | Cagayan State University – Carig Campus | BSECE 2026

## Slide 15
CHAPTER IV — RESULTS & DISCUSSION
Overall Effectiveness — Objectives vs. Outcomes
OBJ
Objective
Key Performance Indicator
Measured Result
Status
OBJ 1
Functional SHM Device
Device operational; continuous data logging across 4 sessions
61,892 records; 100% uptime; all hardware parameters met
✅
OBJ 2
Resonance Frequency Extraction
Consistent frequency identification across repeated tests
Median 5.57–5.94 Hz (All-Axis); 5.93 Hz (Y-session); stable across all sessions
✅
OBJ 3
Real-Time Monitoring Interface
Dashboard operates without failure; live data at 20 Hz
20 Hz polling; 0 transmission failures; 3D simulation responsive to all state changes
✅
OBJ 4
Anomaly Detection Effectiveness
Accurate alert triggering and intensity-mapped visualization
CRIT alerts correctly triggered; 97.6% rate at max excitation; peak intensity = 1.000 detected
✅
Frequency Monitoring SHM System | Cagayan State University – Carig Campus | BSECE 2026

## Slide 16
CHAPTER IV — SUMMARY & CONCLUSIONS
Conclusions
✓
OBJ 1
Functional SHM Device Successfully Developed
A real-time frequency monitoring device was developed using the ESP32-S3 and three MPU-6050 MEMS IMU sensors. The system reliably logged 61,892 data records across four test sessions with 100% transmission success and zero hardware failures.
✓
OBJ 2
FFT-Based Resonance Extraction Validated
The Hamming-windowed 1024-point FFT pipeline successfully extracted dominant resonance frequencies (5.57–5.94 Hz, All-Axis session) consistent with known bridge deck vibration modes (2–10 Hz). The Y-Axis session achieved a median-to-mean difference of only 0.05 Hz, confirming algorithm stability.
✓
OBJ 3
Real-Time Visualization Interface Deployed
The web-based dashboard — hosted on the ESP32-S3 itself — operated at a sustained 20 Hz polling rate with zero dashboard failures. The 3D fabric-ripple simulation and CRIT/WARN/OK state indicators provided clear, real-time representation of vibration activity across all test conditions.
✓
OBJ 4
Anomaly Detection Effectiveness Demonstrated
CRIT-level alerts were triggered correctly in all sessions where excitation exceeded the defined threshold. During Y-Axis maximum excitation, 97.6% of active readings triggered CRIT alerts with no false positives during idle periods — confirming reliable anomaly detection capability.
Frequency Monitoring SHM System | Cagayan State University – Carig Campus | BSECE 2026

## Slide 17
CHAPTER IV — RECOMMENDATIONS
Recommendations for Future Work
1
PCB Miniaturization & Field Deployment
Redesign the custom PCB with proper impedance matching and USB signal integrity to achieve a fully miniaturized, weatherproof, field-deployable unit suitable for actual bridge installation.
2
Multi-Node Sensor Network
Expand the sensor network beyond the current 3-node prototype to cover more structural points along the bridge span, enabling mode shape extraction and spatial anomaly localization.
3
IoT Cloud Integration
Integrate cloud platforms (ThingSpeak, AWS IoT, or similar) to enable long-term data logging, remote access for infrastructure managers, and automated alert notifications to disaster risk officers.
4
Solar/Battery Power Supply
Implement a solar-charged battery system to ensure continuous 24/7 operation in field conditions where grid power is unavailable, particularly for bridges in remote or disaster-prone locations.
5
Machine Learning Integration
Incorporate ML-based anomaly classification (e.g., autoencoders or LSTM models) trained on baseline frequency signatures to enable predictive detection of progressive structural degradation.
6
Full-Scale Field Validation
Conduct full-scale bridge deployment testing under real ambient conditions (traffic, wind, seismic activity) to validate system performance beyond the controlled laboratory environment.
Frequency Monitoring SHM System | Cagayan State University – Carig Campus | BSECE 2026

## Slide 18
THANK YOU
Questions & Discussion
Ayessa Marie Ramos · Jan Clyde Talosig · Shamel Alliyah Senosn · Gemini Almoite
Bachelor of Science in Electronics Engineering · College of Engineering and Architecture
Cagayan State University – Carig Campus · April 2026
61,892
Total Data Records Logged
100%
Transmission Success Rate
5.57–5.94
Hz Structural Resonance